## Slide 1: ANNEALING PROCESS
PRANAV PV
S4 ME
ROLL NO:42

## Slide 2: WHAT IS MEAN BY ANNEALING ?
Annealing,In general,involves heating to a predetermined temperature,holding at this temperature,and finally cooling at a very slow rate
Temperature to be heated & Holding Time
The temperature,to which steal is heated & the holding time are determined by various factors
Chemical composition of steel
size and shape of steel component
final properties desired

## Slide 3: WHAT ARE THE PURPOSES OF ANNEALING ?
1 relive internal stresses developed during solidification,machining,forging,rolling etc
2 improve or restore ductility and toughness
3 enhance machinability
4 eliminate chemical non-uniformity
5 refine grain size
6 reduce gaseous contents in steel.

## Slide 4: Classification of annealing
Based on
1. Temperature of treatment
2. phase transformation that takes place during treatment
3. purpose of the treatment

## Slide 5: 1. Temperature of treatment
Depending on the heat treatment temperature.annealing treatment can be subdivided into three classes
a. full annealing
b. partial annealing
c. subcritical annealing

## Slide 6: FULL ANNEALING
Steel is heated above the upper critical temperature
holding at that temperature
and then cooled very slowly

## Slide 7: PARTIAL ANNEALING
Also known as incomplete annealing or intercritical annealing
involves heating of steel to a temperature lying between lower critical temperature and upper critical temperature
holding at this temperature
And then cooled very slowly

## Slide 8: SUBCRITICAL ANNEALING
Process in which the maximum temperature to which steel is heated is always less than the lower critical temperature
No phase transformation take place
only thermal activated phenomina,such as
recovery
recrystallization
grain growth, and softening occur

## Slide 9: Based on 2. PHASE TRANSFORMATION
1 First type or first-order annealing
first-order annealing is associated with a peculiar charactreistics that heat treatment is performed on the steel with the sole aim of achieving some properties.as such no specific importance is given to phase transformation accompanying the treatment
2 Second type or second-order annealing
End results in the former are essentially due to phase transformation which take place during the treatment
Only temperature above the upper and lower critical temperatures can be utilized for this type of annealing

## Slide 10: BASED ON 3 PURPOSE OF ANNEALING
Depending on the specific purpose ,annealing is classified in to various types
a. DIFFUSION ANNEALING
b.RECRYSTALLIZATION ANNEALING
c.ISOTHERMAL ANNEALING

## Slide 11: DIFFUSION ANNEALING
Also known as homogenizing annealing,is employed to remove any structural non-uniformity.
steel is heated sufficiently above the upper critical temperature(1000-1200”c)
and held at this temperature for prolonged periods, usually 10-20 hours, followed by slow cooling.
Segregated zones are eliminated,and a chemically homogeneous steel is obtained

## Slide 12: Recrystallization annealing
Practically all steels, which have been heavily cold worked, are subjected to this treatment
“ the process consists of heating steel above the recrystallization temperature, holding at this temperature and cooling thereafter. “
…..It results in decrease in hardness or strength and increase in ductility…..
recrystallization annealing temperature, depends on
chemical composition, amount of prior deformation, holding time & initial grain size

## Slide 13: ISOTHERMAL ANNEALING
In this process, hypoeutectoid steel is heated above upper critical temperature and held for some time at that temperature
“ the steel is then cooled rapidly to a temperature less than the lower critical temperature (600-700’c), the steel is held at this temperature till all the austenite gets transformed to pearlite. Then steel is cooled in air ”
This process not only improves machinability in general, but also results in a better surface finish by machining.
Limitation :It is suitable only for small sized components

## Slide 14: thanks