## Slide 1: Cutting Tools
One of most important components in machining process
Performance will determine efficiency of operation
Two basic types (excluding abrasives)
  Single point and multiple point
Must have rake and clearance angles ground or formed on them

## Slide 2: Cutting-Tool Materials
Toolbits generally made of seven materials
  High-speed steel
  Cast alloys (such as stellite)
  Cemented carbides
  Ceramics
  Cermets
  Cubic Boron Nitride
  Polycrystalline Diamond

## Slide 3: Cutting Tool Properties
Hardness
  Cutting tool material must be 1 1/2 times harder than the material it is being used to machine.
Capable of maintaining a red hardness during machining operation
  Red hardness: ability of cutting tool to maintain sharp cutting edge
  Also referred to as hot hardness or hot strength

## Slide 4: Cutting Tool Properties
Wear Resistance
  Able to maintain sharpened edge throughout the cutting operation
  Same as abrasive resistance
Shock Resistance
  Able to take the cutting loads and forces

## Slide 5: Cutting Tool Properties
Shape and Configuration
  Must be available for use in different sizes and shapes.

## Slide 6: High-Speed Steel
May contain combinations of tungsten, chromium, vanadium, molybdenum, cobalt
Can take heavy cuts, withstand shock and maintain sharp cutting edge under red heat
Generally two types (general purpose)
  Molybdenum-base (Group M)
  Tungsten-base (Group T)
Cobalt added if more red hardness desired

## Slide 7: Cast Alloy
Usually contain 25% to 35% chromium, 4% to 25% tungsten and 1% to 3% carbon
  Remainder cobalt
Qualities
  High hardness
  High resistance to wear
  Excellent red-hardness
Operate 2 ½ times speed of high-speed steel
Weaker and more brittle than high-speed steel

## Slide 8: Carbide Cutting Tools
First used in Germany during WW II as substitute for diamonds
Various types of cemented (sintered) carbides developed to suit different materials and machining operations
  Good wear resistance
  Operate at speeds ranging 150 to 1200 sf/min
Can machine metals at speeds that cause cutting edge to become red hot without loosing harness

## Slide 9: Manufacture of Cemented Carbides
Products of powder metallurgy process
  Tantalum, titanium, niobium
Operations
  Blending
  Compaction
  Presintering
  Sintering

## Slide 10: Blending
Five types of powders
  Tungsten carbide, titanium carbide, cobalt, tantalum carbide, niobium carbide
One or combination blended in different proportions depending on grade desired
Powder mixed in alcohol (24 to 190 h)
Alcohol drained off
Paraffin added to simplify pressing operation

## Slide 11: Compaction
Must be molded to shape and size
Five different methods to compact powder
  Extrusion process
  Hot press
  Isostatic press
  Ingot press
  Pill press
Green (pressed) compacts soft, must be presintered to dissolve paraffin

## Slide 12: Presintering
Green compacts heated to about 1500º F in furnace under protective atmosphere of hydrogen
Carbide blanks have consistency of chalk
May be machined to required shape
  40% oversize to allow for shrinkage that occurs during final sintering

## Slide 13: Sintering
Last step in process
Converts presintered machine blanks into cemented carbide
Carried out in either hydrogen atmosphere or vacuum
  Temperatures between 2550º and 2730º F
Binder (cobalt) unites and cements carbide powders into dense structure of extremely hard carbide crystals

## Slide 14: Cemented-Carbide Applications
Used extensively in manufacture of metal-cutting tools
  Extreme hardness and good wear-resistance
First used in machining operations as lathe cutting tools
Majority are single-point cutting tools used on lathes and milling machines