## Slide 1: Engine – the power plant of an automobile - the prime mover

## Slide 2: Heat engines
Internal combustion engines(I C engines)
combustion takes place within the engine.
External combustion engines(E C engines)
combustion takes place outside the engine
Eg. Steam engines, steam turbine, Stirling engine etc.

## Slide 3: Why IC engines?
No heat exchangers involved – improved efficiency – mechanical simplicity
Maximum temperatures exists for very short periods only – higher fluid temperatures possible – higher thermal efficiency
Higher efficiency at lower pressures – less Wt/Power ratios.
Can be designed for smaller outputs with reasonable cost efficiency.

## Slide 4: Another classification
Rotary engines
- Only rotating parts
Reciprocating engines
- Contains reciprocating patrs
Reciprocating IC engines are most widely used for automobiles.

## Slide 6: Drawbacks of reciprocating I C ngines
vibration caused by the reciprocating components.
not possible to use a variety of fuels in these engines.
fuels are relatively more expensive.

## Slide 7: Further classification of IC engines
Based on
Number and arrangement of cylinders
Engine cycle
Number of strokes
Fuel Used
Type of Ignition
Valve arrangement
Type of cooling

## Slide 8: Based on the Number and arrangement of cylinders
Single cylinder engine
Multi cylinder engines
  In line
  Opposed type
  V type
  Radial engine

## Slide 12: Wankel engine