## Slide 1: INTEGRATOR
AKHILJITH P J
ADMISSION NO: M13EE106
S2 M.Tech. POWER ELECTRONICS

## Slide 2: BASIC CIRCUIT
Integrators are used for signal conditioning

## Slide 3
Since the inverting terminal is at virtual ground.
Applying KCL at inverting terminal
i1+i2 = 0

## Slide 4
The output voltage proportional to the integral of input voltage
RC is the time constant of integrator
Also known as inverting integrator
Rcom =R1 for minimizing i/p bias current

## Slide 5: Analysis Of Ideal Integrator

## Slide 6
Bode plot of basic integrator

## Slide 7
fb is the frequency at which gain of the integrator is zero
Fb = 1/2πR1Cf
At lower frequency the capacitor act as an open circuit, resulting an infinite gain
Gain of integrator decreases with increasing frequency

## Slide 8: Limitations of ideal integrator
Ideal integrator is used for a very small frequency range
Offset and bias current contribute an error voltage at the output
Output voltage saturates at lower frequency

## Slide 9: Practical Circuit

## Slide 10
Practical circuit also known as lossy integrator
The resistor Rf limits the low frequency gain to -Rf/R1
Bode plot of lossy integrator

## Slide 11: Analysis of Practical Integrator

## Slide 12: INTEGRATOR WITH REDUCED DC ERROR

## Slide 13
In order to reduce the DC error high feedback is provided
The lowest frequency which can be accurately integrated is limited by the capacitor C2
The general expressions for corner frequencies are obtained by trial and error method
The lowest signal frequency ωs should be at least ten times greater than ω2.

## Slide 14
Initial conditions of integrator

## Slide 15
An integrator is provided with an external circuit to introduce initial conditions
Switch at position 1 gives initial output voltage V0
Switch at position 2 gives integrator output
Capacitor should have low leakage , usually teflon, polystrene are used

## Slide 16: Applications
In analogue computers
In analogue to digital converters
Various signal wave shaping devices
Ramp generator

## Slide 17
THANK YOU