## Slide 1: Industrial Electronics
ANNA JOY
M Tech, P E
NO:6

## Slide 2: V-I converter with floating load V-I converter with grounded load
Voltage to current converter(Transconductance Amplifier)

## Slide 3
V-I Converter with floating load
Vi=iL*R1
iL=Vi/R1

## Slide 4
V-I Converter with grounded load
i1 v1 i21
i2
i1+i2=IL
(Vi-V1)/R +(V0-V1)/R=IL
V1=(Vi+V0-ILR)/2
Gain=1+R/R= 2
V0=2V1=Vi+V0-ILR
Vi=ILR
IL=Vi/R

## Slide 5: FEATURES 1. OTAs are versatile building blocks that intrinsically offer wide bandwidth for many types of amplifiers. 2. The OTA ( voltage-controlled current source) can be viewed as an ideal transistor. 3. OTA is self-biased and has bipolar output, meaning that the output current source can either source or sink the output current. 4. an OTA element simplifies designs of automatic gain control (AGC) amplifiers, light-emitting diode (LED) driver circuits, fast-pulse integrators, control loops for capacitive sensors, and active filters.
Operational Transconductance Amplifier

## Slide 6: Recommended OTA Devices • OPA860 (an OTA and a closed-loop buffer) • OPA861 (an OTA) • OPA615 (a wide-bandwidth dc restoration circuit that contains an OTA and a switching OTA, or SOTA)

## Slide 7: Current-Feedback Amplifier (CFB) Control-Loop Amplifier Sample/Hold Circuit DC-Restore Circuit Instrumentation Amplifier
Advanced uses of OTA

## Slide 8: The CA3080 and CA3080A are similar in generic form to conventional operational amplifiers 1. contains an additional control terminal which enhances the device's flexibility for use in a broad spectrum of applications. 2. communications and industrial applications including modulators, multiplexers, sample-and-hold-circuits, gain control circuits and micro power comparators
CA3080 High-Performance Operational Transconductance Amplifiers

## Slide 9
Current to Voltage Converter (Transresistance Amplifier)
RS
is
V0= -is *Rf
cf

## Slide 10: FEATURES 1. OVER 250kHz TRANSIMPEDANCE BANDWIDTH 2. DYNAMIC RANGE: 5 Decades 3. EXCELLENT LONG-TERM STABILITY 4. BIAS CURRENT: 3pA 5. GAIN BANDWIDTH: 18MHz 6. FAST OVERLOAD RECOVERY 7.SUPPLY RANGE: 2.7V to 5.5V 8.SINGLE AND DUAL VERSIONS
OPA381 and OPA2381

## Slide 11: PRECISION I - V CONVERSION PHOTODIODE MONITORING OPTICAL AMPLIFIERS PHOTOLAB EQUIPMENT
          APPLICATION

## Slide 12: Circuit diagram of OPA381

## Slide 13
DAC USING I-V CONVERTER

## Slide 14: V0=I0*RF
I0=Vref/R1 (D7/2 + D6/4 + D5/8………..+D0/256)

## Slide 15: THANK YOU