## Slide 1: Module 1

## Slide 2
Digital Signal: Advantages
    Cheaper than analog signaling
    Less susceptible to noise interference
Digital Signal: Disadvantages
    Digital signals suffer more from attenuation than analog signals

## Slide 3: Analog transmission
Is a means of transmission of analog signals without regard to their content; The signals may represent analog data (eg: voice) or digital data (eg: binary data that pass through a modem)
Signals will get attenuated after a certain distance
Unfortunately, the amplifier boosts noise components also.

## Slide 4
For analog data, such as voice certain amount of distortions can be tolerated and data can be obtained
For digital data, cascaded amplifiers will introduce errors

## Slide 5: Digital transmission
Is concerned with the content of the signal
A digital signal can be transmitted only a limited distance before attenuation, noise and other impairments affect data integrity
Repeaters are used instead of amplifiers
A repeater receives a digital signal and obtain the pattern of 1s and 0s and then it retransmits new signal

## Slide 6
Same technique is used for analog signal if it carries digital data
The repeater recovers the digital data from the analog signal and generates a new, clean analog signal

## Slide 7: Digital signaling or Analog signaling?
1. Digital technology
    LSI and VLSI technology – reduced cost and size of digital circuitry
2. Data integrity
    Uses repeaters rather than amplifiers
    Effect of noise and other signal impairments are not cumulative

## Slide 8
3. Capacity utilization
    High bandwidth transmission links are available – satellite channels, optical fiber
    High degree of multiplexing is required to utilize such capacity effectively
    Multiplexing can be easily and cheaply achieved in digital domain
4. Security and Privacy
    Encryption techniques can be easily used to provide data security

## Slide 9
5. Integrity
    By treating both analog and digital data digitally, all signals have the same form and can be treated in a similar manner

## Slide 10
 | Analog Signal | Digital Signal
Analog Data | Two Alternatives. (1) Signal occupies the same spectrum as the analog data (No modulation) (2) Analog data are encoded or modulated to occupy a different portion of the spectrum | Analog data is encoded using a codec to produce a digital bit stream
Digital Data | Uses modem to produce an analog signal | Two Alternatives. (1) Signal consists of two voltage levels to represent the two binary values (2) Digital data are encoded to produce a digital signal with desired properties

## Slide 11
 | Analog Transmission | Digital Transmission
Analog Signal | Propagated through amplifiers; same treatment whether it is analog data or digital data. | Assumes that the analog signal represents digital data. Signal is propagated through repeaters. At each repeater, digital data is recovered from the analog signal and generates a new clean analog signal.
Digital Signal | Not used | Digital signal represents a stream of 1s and 0s which may represent digital data or may be an encoding of analog data. At each repeater, stream of 1s and 0s is recovered to generate new digital signal.